## Slide 1: Fuzzy Logic Based Obstacle Avoidance Robot
Hoàng Huy Hoàng – 16020131 – K61-Đ-A-CLC

## Slide 2: Summary
Introduction
Hardware
Fuzzy Logic
Conclusion

## Slide 3
Introduction

## Slide 4: Introduction
- An obstacle avoidance robot based on fuzzy logic.
- Use distance sensor in combination with fuzzy rules to make robot’s movement smooth.

## Slide 5
Hardware

## Slide 6
Hardware
CPU | Atmega328 – 8bit
Frequency | 16MHz
Operating Voltage | 5V DC
Operating current | 30mA
Pins | 14 digital pins, 6 ADC pins
SRAM | 2KB
Flash | 32KB
EEPROM | 1KB
Arduino Uno R3

## Slide 7
Hardware
HC-SR04
- Range: 2 – 300cm
- Principle:
Transmitter
Object
Emitted waves
Reflected waves

## Slide 8
Hardware
Motor Driver L298
- H-bridge circuit.
- Allow control of speed and direction of 2 motors.

## Slide 9
Hardware
Geared DC Motor
- Equipped with gear for extra torque.

## Slide 10
Hardware
18650 Battery
- 18x65mm
- Rechargeable
- 3.7V – 4800mAh

## Slide 11
Fuzzy Logic

## Slide 12
Fuzzy Logic
Left distance sensor
Middle distance sensor
Right distance sensor
Fuzzy logic rules
Left motor
Right motor

## Slide 13
Fuzzy Logic
- 3 inputs and 2 outputs
- Mamdani rule
- Centroid defuzzification

## Slide 14
Fuzzy Logic
- Input membership function

## Slide 15
Fuzzy Logic
- Output membership function

## Slide 16
Fuzzy Logic
-Fuzzy rules
Left sensor | Middle sensor | Right sensor | Left Motor | Right Motor
Near | - | - | Fast | Slow
- | - | Near | Slow | Fast
NOT Near | Medium | NOT Far | Slow | Medium
NOT Near | Medium | Far | Slow | Medium
NOT Far | Medium | NOT Near | Medium | Slow
Far | Medium | NOT Near | Medium | Slow
- | Near | - | Slow | Slow
Medium | - | - | Medium | Slow
- | - | Medium | Slow | Medium

## Slide 17
Conclusion

## Slide 18
Conclusion
- Robot is able to avoid obstacles by applying fuzzy logic.
- Robot speed changes flexibly corresponding to distance to obstacles.
- Combine input from 3 sensors to control robot’s movement.

## Slide 19
Conclusion
- Unable to move backward.
- No use of feedback mechanisms (i.e encoder).

## Slide 20
QUESTION
& ANSWER

## Slide 21
THANK YOU FOR LISTENING !